## Slide 1: Water crisis? What water crisis? Water supply options for a growing Melbourne after the Millennium Drought
Christopher J Walsh
Waterway Ecosystem Research Group,
School of Ecosystem and Forest Sciences
The University of Melbourne
http://urbanstreams.net

## Slide 2: Outline
The Millennium Drought: the problems of relying on river flows for our water supply
Melbourne’s water supply: 2006 – a fateful turning point
What could have been and what might be: a more sustainable approach to urban water supply

## Slide 3
milduramillenniumdrought.weebly.com
The Millennium Drought (2001–2009)
“Worst drought on record for SE Australia”
Dijk et al. (2013) Water Resources Research 49
2001–2006: 18% less rain over the Murray Darling Basin
Gross regional Product dropped by 16%
Flows in the lower Murray dropped by…
82%
Natural flows into the river dropped by 45%
We kept extracting water at much the same rate as normal…

## Slide 4
Why does 18% less rainfall
result in 45% less river flows?
Most rainfall ends up back in the air
Much is stored in the soil and
Transpired by vegetation back to the
atmosphere.
The longer it is dry, the more capacity
soils have to hold back water for
uptake by vegetation
Years of soil water deficit increase the
probability of forest fires

## Slide 5
Melbourne’s water supply and wastewater disposal and treatment system
Dams with capacity for ~10 y demand in a severe drought (with no augmentation)
WWTPs with excellent treatment and little env impact

## Slide 6
Water flowing into Melbourne’s reservoirs 1912–2006 (GL/y)
Long-term average
Average 1997-2006
Year
Volume (GL/y)
2006: a very dry year after 10 quite dry years….
Source: Government of Victoria Sustainable Water Supply: Central Region (2006)

## Slide 7
Water flowing into Melbourne’s reservoirs 1912–2006 (GL/y)
Year
Volume (GL/y)
2006: a very dry year after 10 quite dry years….
An unprecedented decade of demand mainly exceeding inflows
Demand
Long-term average
Average 1997-2006

## Slide 8
Water flowing into Melbourne’s reservoirs 1912–2006 (GL/y)
Year
Volume (GL/y)
2006: a very dry year after 10 quite dry years….
An unprecedented decade of demand mainly exceeding inflows
Worst-case climate-change and demand predictions pointed to
demand exceeding long-term supply by 2020-2030
A short-term augmentation of 50-100 GL/y was needed
Demand
1990s behaviour
2000s behaviour
Projected inflows with climate change
Sources: Melbourne Water (2006) Water Supply Demand Strategy
Jones and Durak (20005) CSIRO

## Slide 9
Water flowing into Melbourne’s reservoirs 1912–2006 (GL/y)
Year
Volume (GL/y)
Feasibility studies commissioned for potential augmentation
100 GL of recycled wastewater from ETP to Cardinia
Extraction from Yarra River at Collingwood
Desalination plant
Demand
1990s behaviour
2000s behaviour
Projected inflows with climated change
Economic winner of
the three.
Politically unpalatable
Not economically
viable
Most expensive,
Most energy intensive
But perceived as most
certain (climate independent)

## Slide 10
Recycled wastewater: the 2006 augmentation proposal
A pipeline from Eastern Treatment Plant to Cardinia:
Cheap because an upgrade to near-potable effluent was already planned and budgeted for.
Energy requirement per kL ~ 30% that required for desal
Politically unpalatable…influence of the Toowoomba referendum?

## Slide 11
The Wonthaggi desalination plant: the successful proposal
Extract seawater from Bass Strait at Wonthaggi
Extract the salt (return concentrated brine to the sea),
pump desalinated water to Cardinia (a service reservoir)

## Slide 12
The Wonthaggi desalination plant: the successful proposal
The dominant water industry advice in 2006 was to develop a ‘portfolio’ of different water sources that included a 50 GL/y desalination plant.
But desal was attractive to the politicians because it was sold as ‘climate independent’
A 150 GL/y plant was ordered.
A new energy-intensive industry when climate change mitigation requires reduction of energy consumption
And the cost of the water that it provides?...

## Slide 13
The Wonthaggi desalination plant: the successful proposal
The retail cost of our water supply system is ~$2.50–$3.00 /kL
The cost of desalinated water was (and continues to be*) claimed as $2–$3 /kL.
But let’s do the maths:
Plant became operational - December 2012
First order of water placed by government –
for 50 GL in Summer 2016-17 (4.2 years later)
Victoria pay Aquasure $620 m/y to operate the plant + ~$200 m for the first order of 50 GL.
= 620 m x 4.2 + 200 m = $2,800 m for 50 GL (or 50 m kL)
= $56 /kL
*Gray (2016) The Conversation.
https://theconversation.com/melbournes-desalination-plant-is-just-one-part-of-drought-proofing-water-supply-55934

## Slide 14
Why did we get a 150 GL plant when we only needed a 50 GL one?
Year
Volume (GL/y)
Demand
1990s behaviour
2000s behaviour
Projected inflows with climated change
In selecting size of plant
a “step change” in runoff
was assumed over best
scientific climate predictions

## Slide 15: The curious turn for water policy in 2006
Technical advice to invest in a portfolio of different augmentation options ignored
A single technology perceived as safe selected, over a cheaper, more sustainable, but less politically palatable alternative
The chosen plant was 2-3 times larger than necessary to meet short-term augmentation needs (reducing incentive to invest in more sustainable augmentation options)
The sizing decision was based on a scenario that was much worse than the worst-case climate change predictions of the time (that remain largely the same today)
In this policy space, climate change predictions were perceived as too optimistic: resulting in immediate, radical action.

## Slide 16
Gleick & Palaniappan M (2010) Proc Natl Acad Sci U S A 107
Trading off water that humans use and water that aquatic ecosystems need
So, to protect our rivers, won’t desal (or wastewater recycling) help to reduce our risk of running our rivers dry?

## Slide 17
Gleick & Palaniappan M (2010) Proc Natl Acad Sci U S A 107
Trading off water that humans use and water that aquatic ecosystems need
No…
Volumes supplied by desal are a tiny fraction of agricultural demands.
In our cities and towns, desal prevents us from solving a more pressing problem, and a seizing a remarkable opportunity…

## Slide 18
Source: Tourism NT
http://www.taevapiltnik.ee/blog/
http://worldlitstories.wikispaces.com
http://media.npr.org
Cairo
Dhaka
Oslo
Darwin
The challenges of managing urban water

## Slide 19: Primary urban water challenges no matter where you are…
Provision of clean water
Treatment and disposal of wastewater
Prevention of flooding
(And usually last priority, protection of the city’s streams, rivers, and downstream lakes/bays/ocean)

## Slide 20
http://gallagher-photo.com
Source: Mandu Essien-Ibok
Source: Bianca Ríos-Touma
China
What happens in cities where wastewater and flooding are
well managed?

## Slide 21
Streams of modern cities with good water supply, sanitation, flood management

## Slide 22
McRae Ck, Yarra Ranges
Why should we care about streams of our cities?
…And what if protecting our cities’ streams can help deliver our other basic needs of water supply and flood protection?

## Slide 23
Streams of modern cities with good water supply, sanitation, flood management

## Slide 24
Streams of modern cities with good water supply, sanitation, flood management
Urban stormwater runoff:
our standard approaches to managing it (for flood protection) degrade our cities’ streams and rivers.*
Alternative approaches could protect and restore them
(and more effectively protect us from floods and provide us with a huge, sustainable water supply…)
*Walsh et al. 2005 J N Am Benthol Soc 24: 706

## Slide 25
Water on a hectare of forest over a year...

## Slide 26
Replace the forest with a building...

## Slide 27
Stormwater runoff is a BIG flow problem

## Slide 28
Keeping stormwater in the catchment...
TF
or (over)-irrigation
Notes: Contrary to popular belief. The best thing we can do for our urban streams is to keep most of the stormwater out of them altogether (so that we can more effectively restore a clean and healthy baseflow).

## Slide 29: Volume reduction and infiltration restoration increasingly difficult at larger scales
Excess runoff to keep out of
waterways by harvesting or
evapo-transpiration losses:
350 - 463 GL/y
(very dry yr – avg yr)
Lost dry-weather flows
to restore through infiltration:
50 - 145 GL/y
(very dry yr – avg yr)
400 – 605 GL/y down our drains
http://urbanstreams.net/tools/melbrunoff/
Notes: Using our maps of impervious, we are able to estimate how much Melbourne’s stormwater system reduces baseflows in our creeks (~80 GL/y across the region), and how much excess problem stormwater flows into the creeks every time it rains (rather than going back into the air like it did when Melbourne was covered by forests): 350 GL/y in a dry year (like the last 4), to 500 GL/y in an average year (like 2010 is shaping to be), to much more in a wet year!

## Slide 30
Year
Volume (GL/y)
Volume of stormwater runoff is much less variable than river runoff.
It has been consistently near Melbourne’s total demand to date
Accounting for urban growth and climate change, future excess stormwater runoff will track demand.
It is a large, reliable, largely unused augmentation source: not using it perpetuates environmental damage
Demand
Excess stormwater
Do we really need a ‘climate-independent’ source of water?
http://urbanstreams.net/tools/melbrunoff/

## Slide 31
Walsh et al. (2012) PLoS ONE 7(9): e45814
Water scarcity? Our rivers experience it before we do

## Slide 32
Walsh et al. (2012) PLoS ONE 7(9): e45814
Urban stormwater runoff: a remarkable opportunity:
Benefits to us of using it match benefits to the environment.
So, why aren’t we doing it?

## Slide 33
Urban stormwater management for flow regime protection requires…
Infiltration systems that restore lost baseflows (of good quality)
and
harvesting systems to keep excess water from streams (indoor use to replace/augment potable water supply or irrigation of open space to replace lost evapotranspiration losses)

## Slide 34: Is it possible?
The Little Stringybark Creek project is showing it is...
urbanstreams.net/lsc
~300 Stormwater control measures installed (230 private properties + public land)
31 ML/y harvested (>75% of the demand of treated properties)
38 ML/y infiltrated (restoration of baseflows and evapotranspiration)
First signs of ecological improvement in the creek
First push by MW to require stormwater harvesting to potable in Sunbury…